## Slide 1: Traffic Volume Estimation & Short-Term Congestion Forecasting USING YOLO AND BYTETRACK
DSCI-41 Capstone Project-1
Focus: Perception & Baseline Pipeline (CP-1)
Project Supervisor: T. Praveen Sharma

## Slide 2: Abstract
The Problem: Reliable vehicle counting is critical for ITS but struggles with occlusions and varying vehicle sizes.
The Solution: A real-time perception framework integrating YOLOv8 (Detection) and ByteTrack (Multi-Object Tracking).
Dataset: Trained and validated using the Barbados Traffic Analysis dataset.
How it Works: YOLOv8 classifies vehicles, while ByteTrack maintains consistent IDs across frames.
The Output: Generates continuous, class-wise time-series traffic volumes for forecasting.

## Slide 3: Problem Statement
Traditional traffic sensors (like loop detectors) are expensive and difficult to maintain.
Camera-based (CCTV) counting is a cheaper alternative, but existing models fail during:
• Heavy occlusion (vehicles blocking other vehicles).
• Adverse weather conditions (Rain, Night, Fog).
• Complex urban intersection layouts.
Current object detectors provide 'hard counts' (1 or 0) which causes data instability during poor visibility, destroying the accuracy of congestion forecasting models.

## Slide 4: Project Objectives
Objective 1 (Phase 1: Perception & Baseline): To develop a highly accurate, real-time vehicle counting baseline using YOLOv8 and ByteTrack. This phase focuses on robust object detection, classifying multiple vehicle types, and maintaining consistent tracking across complex urban camera angles.

## Slide 5: Proposed Methodology
1. Data Input: Continuous video streams from fixed roadside CCTV cameras.
2. Vision Perception Module (YOLOv8):
  Extracts spatial features from video frames.
  Performs high-precision bounding box localization and multi-class classification.
3. Tracking & Association (ByteTrack):
  Takes the bounding boxes from YOLOv8.
  Maintains consistent object identities (IDs) as vehicles move across the screen.
  Mitigates identity loss (ID switching) when vehicles temporarily block each other (occlusion).
4. Output Generation: Produces a continuous, class-wise traffic volume count (e.g., exactly how many cars, buses, and trucks passed through the intersection).